# Text boxes

Project Name:

Kirkham & Wesham Station, Cheshire

Product:

Bespoke Stairwell Canopy and Paragon Seating

Client(s):

Network Rail & J Murphy & Sons

Scope of Project:

The design, manufacture and installation of a bespoke stairwell canopy and paragon seating.

Outline Specification:

- Galvanised steel positioned at 1000mm and 3000mm centres

- 120 degree pitched roof with 3mm clear UV stabilised polycarbonate secured by extruded aluminium H section

- Integral drainage and electrical management

- 6mm UV stabilised polycarbonate glazing secured on all four sides by top and bottom glazing bars and aluminium angle glazing restraints along each vertical edge

- All glazing joints are dry glazed

Project Description:

The brief required the enclosure of an existing stairwell providing pedestrian access to Platforms 1 and 2 from the station building.  The structure has been designed to fix to the existing brick stairwell.

Kirkham & Wesham Station